## Slide 1
Hazard Communication and Enforcement Insights
Susen Trail, CIH
Practical Safety and Health Solutions

## Slide 2: You are at this presentation for one, or more, reasons:
You are proactively obtaining every piece of information you can so you can create an active partnership with your employees to keep your Hazard Communication active and current to protect yourself and others from chemical hazards.
You are responding to observations of failure to implement your Hazard Communication Program, an OSHA violation, near miss, or accident involving chemicals in your workplace.
You need certification maintenance points.
It’s good to take a break and have lunch with your colleagues.

## Slide 3: I am giving this presentation because:
10X more people die each year, in hospitals, hospices, and homes, from occupational exposure to chemicals than are reported by the Bureau of Labor Statistics.
1-3 of the top 10 OSHA General Industry violations every year are for the Hazard Communication standard. 1926.59 ‘adopts’ 1910.1200.
6% of chemicals used in US workplaces have exposure limits.
Notes: I’m no longer in OSHA standard enforcement and, when I was it was in the public sector, more like OSHA Consultation than enforcement.
However, I’m going to do this presentation as if I was still in that role.

## Slide 4: The Arrival

## Slide 5: Common Pitfalls: First Moments On-Site
Employees don’t know who the Safety Manager is.
Employees let you wander around alone.
  Strangers with clipboards.
All indicate no clear plan of action or employee training on what to do when anybody shows up at the front/back/side door asking questions.
Notes: We start looking around and making mental notes before we even enter your workplace.
Not unusual for employees to say they don’t know who the Safety Manager is, we keep changing the definition and description until we get to the right person.

## Slide 6: Common Pitfalls: Opening Conference or Follow Up Meetings
You hand off the person to the complainant because you’re busy.
You have them wait, alone, in your office with relevant information in plain sight.
You accept the implied invitation to commiserate about your problems.
Notes: Has happened, resulted in triple the discovered violations.
If you need someone, call them to come to you. If you have to get something, bring them with you. Never leave them alone.
In vino veritas, yes, we’re kind of colleagues, no, we are not buddies.

## Slide 7: The Walk Through

## Slide 8: The Most Visible ‘Tell’ of Implementation Problems: Labels
  Unlabeled
  Illegible label contents, ink or dirt smeared
  Incomplete labels
  Reused food containers
  Previous label contents still visible
  Container on shelf, pallet, or bench with the label facing away from user

## Slide 9: Employee Work Practices As Compliance Clues
Cluttered workbenches and/or walkways
Overstuffed flammable storage cabinets
Corrosives stored above eye level
Warning signs on doors for hazards no longer present
Employees eating in work areas

## Slide 10: Visual Indicators of Poor Chemical Management
Incompatible chemicals stored side by side on workbenches, on the production floor, in corrosive and flammable chemical cabinets, and in the Chemical Storage Room.
Lack of organized chemical storage in the workplace or storage room.
Ancient chemicals, infrequently or no longer used, pushed to the back of the shelf.
Failure to place the most recently opened chemical X container last so older opened containers are used first
Notes: There be dragons: highway departments and University Chemistry Department professors

## Slide 11: Documentation problems
Inventory:
  Can’t find it
  Didn’t know it was required
  Has names of recently added chemicals scribbled in along the sides
  The guy who was maintaining it doesn’t work here anymore
No training documentation and employees say they weren’t trained
No revision date on the Hazard Communication Program
Notes: The “guy”, meaning they did not assign the job to a Job Title, which is much more likely to last than an employee, will discuss later
Training documentation is not required but now it’s a he said she said as to whether they were trained and if they were trained in the chemical hazards to which they are exposed while working in your workplace.

## Slide 12: Documentation Problems, cont.
SDS book with dusty SDS stuffed in it waiting to be put in order
Employees cannot tell you where SDS are kept
Employee tells you where the book of SDS is kept but didn’t know the system had gone digital about 5 years before
Employee can’t find the SDS for the chemical they’re using in the book or digital file

## Slide 13: More Clues from the Walk Through
Open containers on workbenches
Open paint containers left in corners to dry so the solids and can be thrown away
‘Empty’ chemical containers thrown in the trash without care for compatibility or contribution to air contamination

## Slide 14: The Written Program
You can’t implement what you don’t describe.

## Slide 15: Written Program Red Flags
They can’t find it or it’s “really dusty”
No Job Titles, only names of employees
Named employees no longer work there
No specific procedures for the required tasks
No review/revision/origin date
No definition of non-routine tasks: annual, bi-annual

## Slide 16: The most frequent misstep in writing Hazard Communication Programs:
Not reading the standard, especially definitions, yourself!

## Slide 17: You can create non-Compliant ‘Compliant’ Hazard Communication Programs
While OSHA’s Hazard Communication standard contains the outline of tasks required to create a safe workplace, if you:
Pencil whip a template by putting in your name in every blank line
And/or
2. Fail to consider the conditions/floor plan of your workplace
Your Program will fail within the day or first week.

## Slide 18: Delegation Enables Prevention
Tasks that can, and should, be delegated:
Maintaining a current inventory of chemicals
Maintaining the most recent revision of the SDS
Enforcing the labeling and Safe Work Practices
So you can spend more time on the floor in observation and prevention activities.

## Slide 19: Accurate Communication
The lynch pin for the communication of hazards is the chemical name.
It connects…
The Chemical
To the Inventory
To the Safety Data Sheet
To the label on the container

## Slide 20: Remember this scope
1910.1200(b)(2) This section applies to any chemical which is known to be present in the workplace in such a manner that employees may be exposed under conditions of use or in a foreseeable emergency.
Notes: Known to be present: not “in use” but physically there. In storage, or on the bench top. Important phrase for Inventory.
Workplace means an establishment, job site, or project, at one geographical location containing one or more work areas.
Exposure or exposed includes potential (e.g., accidental or possible) exposure.
Use includes “generate as a byproduct”
Foreseeable emergency means any potential occurrence such as, but not limited to, equipment failure, rupture of containers, or failure of control equipment which could result in an uncontrolled release of a hazardous chemical into the workplace.
Training: in chemicals the employee works with AND AROUND.

## Slide 21: Chemical Inventory
You cannot Communicate the hazards of a chemical if you do not know that it is there!

## Slide 22: 1910.1200(e)(1)(i) Inventory of currently present chemicals
Include the following in the Program and the training:
The process for knowing when a new chemical is going to be purchased/used.
The process for knowing when a new chemical arrives in the facility.
The process for informing the Job Title in charge of the inventory.
The process for informing the Job Title in charge of SDS’.
Notes: This allows for training before employee exposure.
And scheduling disposal of chemicals no longer needed.

## Slide 23: 1910.1200(e)(1)(i) Inventory of currently present chemicals
Include the following in the Program and the training:
The process for knowing when a chemical is no longer going to be purchased/used.
The process for knowing when a chemical is no longer in the facility in any primary or secondary container.
The process for informing the Job Title in charge of the inventory.
The process for informing the Job Title in charge of SDS’.
Notes: This allows for training before employee exposure.
And scheduling disposal of chemicals no longer needed.

## Slide 24: Present Means In Or On Any:
storage room
shed
cabinet
employee’s workbench
any company vehicle
off-site location
Or
behind actively used 55-gallon drums or dusty boxes
in that back room no one goes into anymore

## Slide 25: Not Required, But Should Be
Regular comparison of the Inventory to the chemicals in the workplace.
Regular comparison of the Inventory to the available Safety Data Sheets.

## Slide 26: Source of Information: Safety Data Sheets
The lynch pin for the management of hazards is the SDS.
It contains information to be used for:
Chemical Hazard Information
Chemical management, safe use, storage, etc.
Safe Work Practices, PPE selection, Training
Safe Disposal and/or transport

## Slide 27: The purpose of an SDS is to provide:
Information (temperature, reactivity, etc. conditions) to safely store the chemical
Information to select engineering controls, develop safe work practices, and select PPE
Information on proper handling of the chemical
Information on incompatible chemicals (Hey Bob, it says here that the chemical reacts with the chemicals we currently use for that product, yeah, it creates Cyanide gas and will kill you.)
Training material for employees
Notes: Store in hood, emits a vapor that will explode on contact with hot light bulbs

## Slide 28: AND To Provide:
A resource for employees on chemical hazards
Information for the hospital or medical facility in an emergency.
Information for the Fire Department or Emergency Response Team
A record of employee chemical exposures per 1910.1020(d)(1)(ii)(B) to be archived for 30 years after it is no longer present in your workplace

## Slide 29: New in 2024
The Unknown Toxicant
Manufacturers can say
  “X% of this mixture consists of ingredient(s) of unknown acute (oral/dermal/inhalation) toxicity.”
Notes: At least you get to figure it out for yourselves in a during or soon after exposure.

## Slide 30: Also New in 2024 relevant to Hazard Communication Program Implementation
Classification of physical and health hazards changes for SDS writers
If there is no room for tags, pull out, or fold-back labels:
  Small package, ≤100ml, labels don’t need hazard or precautionary statements
  Very small packages, ≤3ml, only need to be labeled with the name.
SDS: tightened up the concentration of ingredient ranges in Section 3, no more 10-90%

## Slide 31: Managing Your SDS Under Two OSHA Standards 1910.1200 and 1910.1020
1910.1020 Access to employee exposure and medical records
The SDS, or the inventory with where and when the chemical was used, is an employee exposure record and shall be kept for 30 years after the chemical is no longer present in the workplace(s).
1910.1200(g)(5) the chemical manufacturer, importer or employer preparing the SDS shall update it with any new significant information of the hazard, or hazard control, it shall be added to the SDS w/in 3 months and sent with the next shipment
Notes: There are no Letters of Interpretation attached to this new instruction yet.

## Slide 32: Primary Container Labeling
Primary containers come from the manufacturer.
Your responsibility is to:
Ensure the label is not removed
Replace it if you can’t read it
Read and heed the warnings
Get more information from the SDS as needed
Keep that label facing front so you can read it without touching it

## Slide 33: Primary Label Required Content
Name as it is found on the SDS and inventory.
Signal word: Danger or Warning.
Hazard statement.
Pictogram: For emergency responders to see at a distance.
Precautionary statements.
Name, phone number and address of manufacturer.

## Slide 34: Secondary Containers: either use them or don’t
If you use them, you have to have ALL of the information on the primary container label EXCEPT
The name and address of the manufacturer.
When the primary container is empty, one of the secondary container labels has the name and address added, and it becomes primary.

## Slide 35: Secondary Containers Do’s and Don’ts
Food or drink containers are not designed to hold chemicals.
Chemical containers can be reused IF:
They are clean, dry and have no traces of the previous chemical.
The old label is removed or completely covered up (Yay, Duct Tape!).
They do not have a distinctive container shape.
They are relabeled with the required information.
Notes: Some chemicals look like sports drinks, or clear like water

## Slide 36: Label Alternatives
Label alternative(s) that can be used:
Batch labeling: cluster unlabeled secondary containers on or around the primary container
Post the label on the wall above and behind the container
Post the label on the shelf underneath the container
Post the label on the box in which the chemical container is stored
Label the container with a connecting number/letter/name and post the label on the wall with the same number/letter/name

## Slide 37: Labels that ARE NOT ALTERNATIVES:
Why numeric hazard ratings are for emergency responders
Numbers Can Be Seen From A Distance.
NFPA states the hazard rating “Provides information about hazards that occur during emergency response.”
Benzene: Leukemia
Hydrochloric acid: burns
Notes: This rates “acute toxicity” effects from a single exposure or multiple exposures in a short time.
This is not representative of occupational exposure in the day-to-day workplace.

## Slide 38: These ARE NOT Alternatives: Example - Benzene
Benzene By The Numbers
American Coatings Association, HMIS label, states “The hazard rating (0-4) in the Health block are used to communicate information on immediate health effects, including irritants, skin sensitizers, corrosives and acute toxicity.”
This is why Benzene, which can give you leukemia, is a 2 out of 4.
For more information: osha.gov/sites/default/files/publications/OSHA3678.pdf
HMIS
2 – Health Hazard: Temporary or minor injury may occur.
NFPA
2 – Health Hazard: Can Cause temporary incapacitation or residual injury.

## Slide 39: Pictograms
Vague Much?
This pictogram lets you know that the chemical can do one or more of 6 things somewhere inside of your body.
This pictogram says the chemical can support or start a fire one of 7 ways.
This one says “Warning” about over 5 things

## Slide 40: Pictograms, cont.
GHS Pictograms
Ozidizers
Gasses Under
Pressure
Acute Toxicity
(Severe)
Explosives
Self-Reactives
Organic Peroxides
Corrosives
Irritant
Dermal Sensitizer
Acute Toxicity
Narcotic Effects
Respiratory Tract Irritation
Carcinogen
Respiratory Sensitizer
Reproductive Toxicity
Target Organ Toxicity
Mutagenicity
Aspiration Toxicity
Flammables
Self-Reactives
Pyrophorics
Chemically unstable gas
De-sensitized Explosives
Self-Heating
Emits Flammable Gas
Notes: Acetone peroxide forms highly shock-sensitive crystals upon evaporation and exposure to air; it’s one of the most dangerous and unpredictable explosives known.
The peroxide bond is very weak and easily breaks, releasing a large amount of energy, creating a chain reaction almost instantaneously: detonation.

## Slide 41: So, Where Do I Get My Information?
GHS Hazard Statements, Hs, and Precautionary statements, Ps are required to be on the primary container label and in Section 2 of the Safety Data Sheet.
The Hazard statement may or may not have the number:
H350, but will say: May be carcinogenic
Same with the Precautionary statements: 201, Obtain special instructions before use
Use your words!!

## Slide 42: Remember this scope applies to training
1910.1200(b)(2) This section applies to any chemical which is known to be present in the workplace in such a manner that employees may be exposed under conditions of use or in a foreseeable emergency.
Notes: Known to be present: not “in use” but physically there. In storage, or on the bench top. Important phrase for Inventory.
Workplace means an establishment, job site, or project, at one geographical location containing one or more work areas.
Exposure or exposed includes potential (e.g., accidental or possible) exposure.
Use includes “generate as a byproduct”
Foreseeable emergency means any potential occurrence such as, but not limited to, equipment failure, rupture of containers, or failure of control equipment which could result in an uncontrolled release of a hazardous chemical into the workplace.
Training: in chemicals the employee works with AND AROUND.

## Slide 43: Training, your training has to include the following for their work area
OPERATIONS in their work area where chemicals are present, not just the chemicals they use
How to detect the presence or release of a chemical in their work area
Measures an employee can take to protect themselves from the specific chemical hazards in their work area 1910.1200(h)(3)(ii) and (iii)
  Safe Work Practices
  Emergency Procedures
  PPE
  Labeling system
  Safety Data Sheet
  How to obtain and use appropriate hazard information
Notes: Wouldn’t it be handy if an employee observed a spill from a source along their path to their work area

## Slide 44: Work Area
A room or a defined space in a workplace where hazardous chemicals are produced or used AND where employees are present.
There are rooms and where only designated employees are expected to go such as inside welding areas, or paint spray booths.
However, employees walk by or enter areas where chemicals are stored and can act as an early warning system to the release of chemicals that could have serious or far-ranging effects.

## Slide 45: 1910(e)(1)(ii) Non-routine tasks
Your program shall contain the methods you plan to use to inform employees of the hazards of non-routine tasks
This means: What Job Title shall inform them
And
The definition of a Non-Routine task. Weeks between performance, months, half a year?
How long until the employees forget what you trained them?

## Slide 46: 1910(e)(1)(ii) also requires you to train employees in
The hazards associated with chemicals in unlabeled pipes in their work areas.
Your Program should include what those pipes look like (paint color, etc.), where they are, and which employees, by Job Title or other specifically identifying method, working underneath or near them should be trained in their hazards.
Either in the Program or in an easy to update appendix to the program.

## Slide 47: 1910.1200(e)(2) Multi-employer workplaces
Remember, 1926.59 refers to/implements 1910.1200. The Hazard Communication Program shall describe how:
Access to SDS for each chemical that the other employer’s employees may be exposed to while working.
Information regarding precautionary measures the other employees may use to protect themselves during normal and foreseeable emergencies.
Information about the labeling system being used.
Notes: In a fire go down the left aisle as he right aisle is where all our flammables are stored.

## Slide 48: 1910.1020(g) Access to Employee Exposure and Medical Records
The training topics shall include:
The existence, location, and availability of any records covered by this standard.
The person responsible for maintaining and providing access to records; and
Each employee's rights of access to these records

## Slide 49: What’s that mean?
If I, as an Industrial Hygienist, provide you with a report of data from air or noise data assessing employee exposures, then my report must meet the detailed requirements of 1910.1020 as an employee exposure record and it must be kept for 30 years.
If your SDS shows changes in chemical hazards sufficient to change, or add to, the health risks from chemical exposure, you need to clearly identify when that change was made by archiving the SDS that listed the previous hazards and replace it with the new SDS that details the hazards of the chemical employees to which they are now exposed.
Notes: Acid to Base, still corrosive but not the same chemical compatibilities, so good to advise production engineers.
Acid to absorbs through skin to give you a disease, quite different hazard, requires retraining.

## Slide 50: SDS Changes: Important Information, Required 1910.1020 Archive Maintenance
Change from Acid to Base, still corrosive. Assess effect on production, potential explosion has killed 3 employees and destroyed 1/3 of plant.
SDS now lists absorb through skin hazard. Update training, archive SDS you have and replace it with the updated SDS.
SDS update regards new ownership, what does legal want you to do.
SDS update regards only new address, update onsite SDS record, replacing archived SDS up to legal.
Notes: And so on.

## Slide 51: It all boils down to this:
If your procedures
Are generic, rather than designed for your facility
Assign tasks to ‘Fred Jones,’ rather than to a Job Title
Are not written down, clearly and specifically, rather than ‘The Inventory must be kept up to date’
Then your Program may be compliant, but your workplace is not.

## Slide 52: Questions?
Thank you very much, if you think of a question later you can reach me at:
      cih@psahs.com
      920-944-9143
      For private sector specific inspections, go to osha.gov/enforcement/directives/cpl-02-02-038

## Slide 53: How to read an OSHA standard
1910 is called a Part.
1910.1200 Hazard Communication standard is called a “section”.
1910.1200(b) is called a paragraph
Shall is required, Should is a good idea.

## Slide 54: How to read an OSHA standard, cont.
Read the Scope and Application, usually first, sometimes last
1910.146 Scope and application. This section contains requirements for practices and procedures to protect employees in general industry from the hazards of entry into permit-required confined spaces.
If you do not have a confined space with a hazard then you do not fall within the scope of the standard.

## Slide 55: How to Read an OSHA Standard
Sometimes there are scopes for the application of a paragraph.
1910.1200(b) Scope and application
(b)(3) This section applies to laboratories only as follows:
If you don’t have a laboratory you can skip down to (b)(4) and so on.